## Slide 1: Multi-Product Supply Chain Optimization
Konstantin Pielmaier
Semester Project
30. October 2025, Zurich
Notes: Thanks for coming to the midterm presentation of my semester project on the topic of Multi-Product Supply Chain Optimization of Energy Systems supervised by Gabriel.

## Slide 2: Motivation – Overcoming the central planner approach
[1] Yang Shu et al., “Overcoming the central planner approach – Bilevel optimization of the European energy transition,” iScience, vol. 27, no. 7, 2024, https://doi.org/10.1016/j.isci.2024.110168
minimize total system cost
subject to supply = fixed demand
Notes: The motivation for my semester project is overcoming the central planner approach frequently used in energy system planning. In most of these optimization models, demand is fixed and supplied at minimum total system cost. This assumes there is a central planner that is capable of making all decision.

## Slide 3: Motivation – Overcoming the central planner approach
[1] Yang Shu et al., “Overcoming the central planner approach – Bilevel optimization of the European energy transition,” iScience, vol. 27, no. 7, 2024, https://doi.org/10.1016/j.isci.2024.110168
competing stakeholders
Consumers
Suppliers
Notes: However, this does not reflect how modern power markets operate, where stakeholders make decentral decisions.

## Slide 4: Motivation – Overcoming the central planner approach Bilevel optimization of the European energy transition
Is central planning a good enough approximation?
installed capacity distribution ±40%
average market clearing price +40%
[1] Yang Shu et al., “Overcoming the central planner approach – Bilevel optimization of the European energy transition,” iScience, vol. 27, no. 7, 2024, https://doi.org/10.1016/j.isci.2024.110168
Notes: Climate change  multinational challenge  joint GHG reduction target
EU carbon/electricity market bilevel optimization  cost-optimal transition pathway
National interest  minimize energy supply cost  competition between countries

## Slide 5: Motivation – Overcoming the central planner approach Bilevel optimization of the European energy transition
Limitation:
bilevel  computationally complex
only major strategic decisions at country scale
Outlook:
investigate competing industry stakeholders
better market effects
even more complex
Further:
multi-sector coupling
spatio-temporal resolution
uncertainty
[1] Yang Shu et al., “Overcoming the central planner approach – Bilevel optimization of the European energy transition,” iScience, vol. 27, no. 7, 2024, https://doi.org/10.1016/j.isci.2024.110168
Notes: Bilevel  single-level MILP

## Slide 6
Modelling
Integration
Starting point EnergyScope TD
Framework
Multi-product
supply chain
Motivation Overcome central planner

## Slide 7
Modelling
Integration
Starting point EnergyScope TD
Framework
Multi-product
supply chain
Motivation Overcome central planner
Notes: Where to start from?
We already have a model which is able to perform a lot of these tasks (multi-sector coupling, spatio-temporal resolution, uncertainty)
So, we don’t need to build something from the ground up, instead rather use EnergyScope TD as a starting point

## Slide 8: Starting point – EnergyScope TD
[2] G. Limpens, S. Moret, H. Jeanmart, and F. Maréchal, “EnergyScope TD: A novel open-source model for regional energy systems,” Applied Energy, vol. 255, 2019, https://doi.org/10.1016/j.apenergy.2019.113729
Goal: long-term strategic energy system planning
Investment & operation
optimization
Typical day (TD)
 fast!  uncertainty
Target year (“snapshot”)
Hourly resolution
Objective:
min total system cost
s.t. supply = fixed demand
Layer balance
Multi-sector
coupling
Storage
Implementation:
open-source
linear program (LP)
central planner
technologies

## Slide 9: Starting point – EnergyScope TD
Electric Vehicle
Demand = Consumer
Wind farm
Technology = Processor
Electricity
Output Product
Wind
Input Product
Wind
Resource = Supplier
technologies
Notes: What are the corresponding stakeholders in EnergyScope TD?
Resources  e.g. electricity/natural gas grid, uranium, wind
Technologies  processors  e.g. CCGT, nuclear, wind powerplant
Demand  consumers  e.g. electricity load
?  products  electricity, natural gas, uranium, wind

## Slide 10: Starting point – EnergyScope TD
technologies
Electric Vehicle
Demand = Consumer
Wind farm
Technology = Processor
Electricity
Output Product
Wind
Input Product
Wind
Resource = Supplier
Grid
Transporter
Electricity
Transport product
Notes: To incorporate the spatial-resolution…

## Slide 11
Modelling
Integration
Starting point EnergyScope TD
Framework
Multi-product
supply chain
Motivation Overcome central planner
Notes: Now that we have identified the stakeholders in EnergyScope TD, we need a market framework that models their competition…

## Slide 12: Framework – Multi-Product Supply Chain Optimization
Electric Vehicle
Consumer
Wind farm
Processor
Wind
Supplier
Grid
Transporter
max profit
s.t. capacity
max profit
s.t. capacity
max profit
s.t. capacity
max profit
s.t. capacity
[3] P. A. Tominac and V. M. Zavala, “Economic properties of multi-product supply chains,” Computers & Chemical Engineering, vol. 145, 2021, https://doi.org/10.1016/j.compchemeng.2020.107157
Stakeholder Graph
Notes: At the university of Wisconsin-Madison in the lab of Professor Zavala, they developed a multi-product supply chain optimization framework using a stakeholder graph. Each stakeholder wants to maximize their own individual profit subject to their capacity constraint.

## Slide 13: Framework – Multi-Product Supply Chain Optimization
max profit
s.t. capacity
max profit
s.t. capacity
max profit
s.t. capacity
max profit
s.t. capacity
min capacity margin
s.t. economic driving force
max social welfare
s.t. balance, capacity
Coordinated Market Auction
Independent System Operator (ISO)
resource allocation
bidding information
market prices
bidding information
physical primal
economic dual
Value
Capacity
Notes: The stakeholders are part of a coordianted market auction. The stakeholders submit their bidding information to the ISO.

## Slide 14
Processors
max profit
s.t. capacity
Transporters
max profit
s.t. capacity
Suppliers
max profit
s.t. capacity
Consumers
max profit
s.t. capacity
ISO (economic dual clearing)
min capacity margin
s.t. economic driving force
ISO (physical primal clearing)
max social welfare
s.t. balance, capacity
resource allocation
bidding information (capacity, value)
market clearing prices
bidding information (capacity, value)

## Slide 16: Framework – Multi-Product Supply Chain Optimization
[3] P. A. Tominac and V. M. Zavala, “Economic properties of multi-product supply chains,” Computers & Chemical Engineering, vol. 145, 2021, https://doi.org/10.1016/j.compchemeng.2020.107157
decentral LP
 scalable!
max social welfare
s.t. balance, capacity
max stakeholder profit
s.t. capacity
min capacity margin
s.t. economic
driving force
Notes: This is the mathematical formulation. I want you to focus on the three essential parts maximizing social welfare, maximizing stakeholder profit, and minimizing capacity margins. Most importantly, the entire framework is a linear meaning we have a scalable decentral linear program.

## Slide 17: Framework – Multi-Product Supply Chain Optimization
[3] P. A. Tominac and V. M. Zavala, “Economic properties of multi-product supply chains,” Computers & Chemical Engineering, vol. 145, 2021, https://doi.org/10.1016/j.compchemeng.2020.107157
Economic
properties
4. Revenue adequacy
3. Competitive
equilibrium
2. No stakeholder
loses money
1. Market clearing
prices are bound
physical
economic
Notes: Beyond being linear, the market also makes sense. To this end, the Zavala paper mathematically derives important economic properties of the market.

## Slide 18
Modelling
Integration
Starting point EnergyScope TD
Framework
Multi-product
supply chain
Motivation Overcome central planner
Notes: Now that we have a starting point and framework to overcome the central planner assumption…

## Slide 19: Modelling – Incorporating EnergyScope TD
Demand
quantity
[MW]
price
[€/MWh]
linear  social welfare quadratic
fixed   economic properties 1, 2, 3, 5
value-of-lost-load (VOLL) 
Notes: 1 bound prices, 2 positive profits, 3 competitive equilibrium, 4 revenue adequacy, 5 market-activating bids
“This is precisely how coordinated electricity markets operate in the US; here, satisfaction of demands is enforced by defining a bid known as the value-of-lost-load (VOLL).
This bid captures the value of electricity to society and is set to values that are as high as 1000 USD per MWh (the average cost in the US is around 10 USD per MWh).
Effectively, VOLL operates as a market-activating bid that promotes provision of electricity. This is used, for instance, as a mechanism to enforce provision of electricity in remote areas.
Effectively, market activating bids enforce participation but this is done via economic incentives (not by enforcing constraints). This approach preserves the economic properties of the market.”
Alternative stakeholder
Others: d demand
Place in Literature – Market Resolution
Game theory  leader-follower relationships
Direct contract negotiation (Stackelberg)  non-linear
Explicit price and quantity  demand-price relationships  non-linear
Auction  market price relationships (Cournot, Bertrand competition)
Stakeholders submit bidding information (capacity, value)  linear
Assumptions
Accurate stakeholder information
No disturbances or failure  deterministic
1 bound prices, 2 positive profits, 3 competitive equilibrium, 4 revenue adequacy, 5 no transport cycles
“This is precisely how coordinated electricity markets operate in the US; here, satisfaction of demands is enforced by defining a bid known as the value-of-lost-load (VOLL).
This bid captures the value of electricity to society and is set to values that are as high as 1000 USD per MWh (the average cost in the US is around 10 USD per MWh).
Effectively, VOLL operates as a market-activating bid that promotes provision of electricity. This is used, for instance, as a mechanism to enforce provision of electricity in remote areas.
Effectively, market activating bids enforce participation but this is done via economic incentives (not by enforcing constraints). This approach preserves the economic properties of the market.”
Alternative stakeholder
Others: d ≤ demand
Place in Literature – Market Resolution
Game theory  leader-follower relationships
Direct contract negotiation (Stackelberg)  non-linear
Explicit price and quantity  demand-price relationships  non-linear
Auction  market price relationships (Cournot, Bertrand competition)
Stakeholders submit bidding information (capacity, value)  linear
Assumptions
Accurate stakeholder information
No disturbances or failure  deterministic

## Slide 20: Modelling – Incorporating EnergyScope TD
Demand
Investment  new objective function term: ,
[4] F. Kachirayil, D. Huckebrink, V. Bertsch, and R. McKenna, “Trade-offs between system cost and supply security in municipal energy system design: An analysis considering spatio-temporal disparities in the value of lost load,” ESA Working Paper Series, 2024.
quantity
[MW]
price
[€/MWh]
value-of-lost-load (VOLL)

objective function penalty:
Notes: Capital Recovery Factor (CRF)
𝑉𝑂𝐿𝐿(𝑎𝑣𝑒𝑟𝑎𝑔𝑒 𝐺𝑒𝑟𝑚𝑎𝑛𝑦)=11.03 €/𝑀𝑊ℎ
Capital Recovery Factor (CRF)

## Slide 21: Modelling – Incorporating EnergyScope TD
[5] P. A. Tominac, W. Zhang, and V. M. Zavala, “Spatio-temporal economic properties of multi-product supply chains,” Computers & Chemical Engineering, vol. 159, 2022, https://doi.org/10.1016/j.compchemeng.2022.107666
Space-Time
Node
Dynamic
Supply Chain
Time Series
capacity factor
demand
Storage
new stakeholder:
 temporal transporter
EnergyScope TD
hours h
typical days td
Notes: Thinking of demand/investment leads us to…

## Slide 22: Framework – Spatio-temporal
[5] P. A. Tominac, W. Zhang, and V. M. Zavala, “Spatio-temporal economic properties of multi-product supply chains,” Computers & Chemical Engineering, vol. 159, 2022, https://doi.org/10.1016/j.compchemeng.2022.107666
SI example validation


## Slide 23
Modelling
Integration
Starting point EnergyScope TD
Framework
Multi-product
supply chain
Motivation Overcome central planner

## Slide 24: Outlook
Bidding information
value
capacity
Storage
daily (battery)
seasonal (PHES)
Case Study
benchmark
validation
Conclusion
viable?
useful?
Notes: Bidding information  bid value (resource cost, operating cost, etc.) and capacity (actually quite clear?) implicit in EnergyScope TD?  validation, other sources?
Storage  efficiency, periods, state of charge (SoC)  clean/smooth integration tricky
Case study  EnergyScope TD, waste management economy, waste-to-energy (biogas, electricity)
Conclusion  market-activating bids, market price(, investment/operation decision-making)

## Slide 25: Thanks for your attention! Feedback/Questions?

## Slide 26: References
[1] Yang Shu et al., “Overcoming the central planner approach – Bilevel optimization of the European energy transition,” iScience, vol. 27, no. 7, 2024, https://doi.org/10.1016/j.isci.2024.110168
[2] G. Limpens, S. Moret, H. Jeanmart, and F. Maréchal, “EnergyScope TD: A novel open-source model for regional energy systems,” Applied Energy, vol. 255, 2019, https://doi.org/10.1016/j.apenergy.2019.113729
[3] P. A. Tominac and V. M. Zavala, “Economic properties of multi-product supply chains,” Computers & Chemical Engineering, vol. 145, 2021, https://doi.org/10.1016/j.compchemeng.2020.107157
[4] F. Kachirayil, D. Huckebrink, V. Bertsch, and R. McKenna, “Trade-offs between system cost and supply security in municipal energy system design: An analysis considering spatio-temporal disparities in the value of lost load,” ESA Working Paper Series, 2024.
[5] P. A. Tominac, W. Zhang, and V. M. Zavala, “Spatio-temporal economic properties of multi-product supply chains,” Computers & Chemical Engineering, vol. 159, 2022, https://doi.org/10.1016/j.compchemeng.2022.107666

## Slide 27: Framework – Supply Chain Stakeholder Graph
Node-based
Product-based
[3] P. A. Tominac and V. M. Zavala, “Economic properties of multi-product supply chains,” Computers & Chemical Engineering, vol. 145, 2021, https://doi.org/10.1016/j.compchemeng.2020.107157